## Slide 1: PUMP OPERATIONS
Safety Training for New Employees
Manufacturing Operations Department

## Slide 2: Training Objectives
After completing this training, you will be able to:
  Identify hazards associated with pump operations
  Apply proper Lockout/Tagout (LOTO) procedures
  Select and use appropriate PPE
  Recognize abnormal operating conditions
  Respond appropriately to emergencies

## Slide 3: Pump System Hazards
Rotating Equipment:
  Catch points with couplings, exposed shafts can pull in clothing or hair
High Pressure:
  120 PSI discharge - pinhole leaks can inject fluid under skin
Electrical:
  460V 3-phase motors - risk of shock, arc flash
Noise:
  85-95 dBA during operation - hearing protection required
Hot Surfaces:
  Bearing housings can reach 180°F - burn hazard

## Slide 4: Lockout/Tagout (LOTO) Procedure
NEVER work on equipment without LOTO!
1. Notify affected employees
2. Shut down equipment normally
3. Isolate all energy sources
4. Apply YOUR personal lock and tag
5. Release stored energy
6. Verify zero energy state

## Slide 5: Required Personal Protective Equipment (PPE)
Minimum PPE (always)
  Safety glasses, Steel-toed boots, Hearing protection in pump room
Maintenance Work
  Face shield (for hydraulic work), Leather gloves, Long sleeves
Electrical Work
  Arc-rated gloves (Class 00 minimum), Face shield with arc rating

## Slide 6: Normal Operating Parameters
What to check during rounds:
  Discharge pressure: 100-120 PSI (normal)
  No unusual vibration or noise
  No leaks from seals or connections
  Bearing temperature: warm to touch, not hot
  Report anything abnormal immediately!

## Slide 7: Emergency Procedures
Major Leak/Spray:
  Press E-STOP, Evacuate area, Call 5555
Fire:
  Activate alarm, Evacuate, Call 5555, Use extinguisher if trained and safe
Injury:
  Call 5555 immediately, Do not move injured person unless immediate danger
Equipment Failure:
  Press E-STOP, Notify supervisor, Do NOT attempt to restart

## Slide 8: Emergency Contact Numbers
Emergency Services: 5555
Maintenance Supervisor: 5556
Safety Officer: 5557
Plant Manager: 5558
Posted at all stations and on your badge!

## Slide 9: Remember: Safety First!
Key Takeaways:
  Never bypass safety devices
  Always use LOTO before maintenance
  Wear appropriate PPE at all times
  Report all hazards, near-misses, and incidents
  When in doubt, STOP and ask!
  Questions? Contact Safety Officer at ext. 5557